## Slide 1
ROAD CRACK DETECTION
USING OPENCV
Traditional computer vision for road-surface inspection
INPUT IMAGE
FEATURE OUTPUT
IMAGE PROCESSING · EDGE DETECTION · ORB FEATURES
Presented by :
Pragyan Garg (20233212)
Pushpraj Singh (20233226)
Nishan Patgiri (20233204)
Piyush Rai (20233210)
01 / 20

## Slide 2
The problem
Why early crack detection matters
CRACK DETECTION • OPENCV
02 / 20
Road cracks start small. Delayed inspection can make maintenance more expensive and difficult.
Manual inspection
Large road networks take time and labour to inspect consistently.
Changing surfaces
Shadows, rough asphalt and lighting can make cracks hard to spot.
Need for prioritisation
Potential defects should be found early so experts can assess and repair them.
Goal: help inspectors locate suspicious crack patterns from road images.

## Slide 3
What is this project?
A lightweight, rule-based computer-vision pipeline
CRACK DETECTION • OPENCV
03 / 20
ROAD PHOTO
OpenCV pipeline
Enhance image, detect edges, connect gaps and extract features.
FEATURE OUTPUT
No model training is required: the script uses predefined image-processing algorithms and ORB feature extraction.

## Slide 4
Objectives & scope
What the current implementation aims to do
CRACK DETECTION • OPENCV
04 / 20
01 Enhance the image
Convert to grayscale and reduce unwanted pixel variation.
02 Highlight crack edges
Use edge detection to expose thin, high-contrast structures.
03 Improve continuity
Close small gaps in the detected edge map.
04 Extract visual features
Use ORB keypoints/descriptors for further image analysis.
Scope note: the current script highlights candidate structures; it does not train a classifier or measure crack depth.

## Slide 5
The methodology
From a road photograph to a feature-highlighted output
CRACK DETECTION • OPENCV
05 / 20
01
Input
Road image
02
Grayscale
Intensity image
03
Blur + log
Reduce noise / enhance
04
Bilateral
Smooth, preserve edges
05
Canny
Detect edges
06
Closing
Connect small gaps
07
ORB
Extract keypoints
08
Output
Save feature image
The script shown in the ZIP processes Cracked_07.jpg and writes CrackDetected-7.jpg.

## Slide 6
System architecture
Four simple layers: input, processing, feature extraction and output
CRACK DETECTION • OPENCV
06 / 20
INPUT LAYER
Image file loaded with cv2.imread()
PRE-PROCESSING
Grayscale → 3×3 averaging blur → logarithmic transform → bilateral filter
DETECTION & FEATURES
Canny edge detection → morphological closing → ORB keypoints/descriptors
OUTPUT LAYER
Draw keypoints, save JPG with cv2.imwrite(), display with Matplotlib
Core libraries: Python · NumPy · OpenCV · Matplotlib

## Slide 7
Stage 1: Image capture
High-quality input images are essential
CRACK DETECTION • OPENCV
07 / 20
Example input A
Example input B
Capture considerations
Good focus, sufficient resolution and even lighting improve the chance of detecting crack details.

## Slide 8
Stage 2: Grayscale & averaging blur
Simplify intensity information and reduce small-scale noise
CRACK DETECTION • OPENCV
08 / 20
Original image
Grayscale
3×3 average blur
Why grayscale?
Uses brightness instead of three colour channels.
Why blur?
Reduces small intensity variations before edge detection.

## Slide 9
Stage 3: Logarithmic transformation
Enhance intensity differences in darker regions
CRACK DETECTION • OPENCV
09 / 20
Before: blurred grayscale
After: log-transformed
Typical formula: s = c · log(1 + r) | r = input intensity, c = scaling factor
It changes contrast; it does not identify a crack on its own.

## Slide 10
Stage 4: Bilateral filtering
Smooth similar pixels while preserving strong boundaries
CRACK DETECTION • OPENCV
10 / 20
Log transformed
Bilateral filtered
Key idea
The filter considers both spatial distance and intensity similarity, reducing blur across strong edges.

## Slide 11
Stage 5: Canny edge detection
Find rapid changes in image intensity
CRACK DETECTION • OPENCV
11 / 20
Filtered image
Canny edge map
1 Gradient
Measure intensity change.
2 Thin edges
Non-maximum suppression.
3 Thresholds
Keep strong/connected edges.

## Slide 12
Stage 6: Morphological closing
Connect small gaps in the detected edge structures
CRACK DETECTION • OPENCV
12 / 20
Before closing
After closing
Dilation
Expands foreground pixels; nearby segments can join.
Then erosion
Shrinks the expanded result while retaining some connections.

## Slide 13
Stage 7: ORB feature extraction
ORB = Oriented FAST and Rotated BRIEF
CRACK DETECTION • OPENCV
13 / 20
Closed edge map
Keypoints drawn on output
FAST
Finds distinctive keypoint locations.
BRIEF descriptor
Represents local appearance as a compact binary descriptor.

## Slide 14
The full processing pipeline
What the script does in sequence
CRACK DETECTION • OPENCV
14 / 20
01
Read
cv2.imread
02
Gray + blur
cv2.cvtColor / cv2.blur
03
Log transform
NumPy log
04
Bilateral
cv2.bilateralFilter
05
Edges
cv2.Canny
06
Closing
morphologyEx
07
ORB
detectAndCompute
08
Save
cv2.imwrite
The current script reads one configured sample image and writes one output file.

## Slide 15
Results & observations
Sample outputs included in the project ZIP
CRACK DETECTION • OPENCV
15 / 20
INPUT
CANNY EDGES
ORB OUTPUT
What the output shows
Candidate edges and visual keypoints are highlighted for inspection.
Reported performance
README suggests 80–90% may be possible on clear images; evaluation details are not provided.

## Slide 16
How should performance be evaluated?
Visual output alone is not a validated accuracy score
CRACK DETECTION • OPENCV
16 / 20
Precision
Of the regions marked as cracks, how many are truly cracks?
Recall
Of all real crack regions, how many did the system detect?
F1-score
Balances precision and recall in one measure.
Recommended evaluation
• Create a labelled test set with cracked and non-cracked images.
• Compare detections against ground-truth crack masks or labels.
• Report false positives, false negatives, precision, recall and F1.
• Test under different lighting, textures and image resolutions.
The current README does not document this evaluation protocol.

## Slide 17
Technology stack
Each library has a focused role
CRACK DETECTION • OPENCV
17 / 20
Python
Runs the processing script
OpenCV
Image transforms, Canny, closing, ORB
NumPy
Logarithmic intensity transform and arrays
Matplotlib
Displays original and output images
No training dataset, model weights, GPU, web server or database is required by this script.

## Slide 18
Challenges & limitations
What can affect the quality of detection?
CRACK DETECTION • OPENCV
18 / 20
Shadows and lighting
Strong shadows can resemble cracks; uneven light changes contrast.
Road texture
Gravel, patches and rough asphalt may create unwanted edges.
Parameter sensitivity
Canny thresholds and kernel sizes affect the output.
Not a crack classifier
ORB detects keypoints; it does not decide whether a feature is a crack.
Current output should support inspection, not replace engineering assessment.

## Slide 19
Future scope & key takeaways
A foundation that can be extended
CRACK DETECTION • OPENCV
19 / 20
Batch processing
Process all images in a folder rather than one hard-coded sample.
Crack segmentation
Produce a clearer crack mask and estimate affected area.
Classification
Add a trained model if reliable crack/non-crack or crack-type labels are needed.
Better validation
Benchmark against labelled data across diverse conditions.
TAKEAWAYS
• Traditional computer vision — no model training in the current script.
• Preprocessing → edge map → morphological closing → ORB features.
• Image quality matters; reported accuracy needs a documented test.

## Slide 20
THANK YOU
Questions & Discussion
Crack Detection Using OpenCV · Traditional Image Processing
20 / 20